Dr. Geng Anli,

President, BioEnergy Society of Singapore

Senior Lecturer and Technology Development Manager, School of Life Sciences and Chemical Technology, Ngee Ann Polytechnic. Tel: (65) 64608617; Fax: (65) 64679109; Email: gan2@np.edu.sg

Dr. Geng Anli currently holds the President position in BioEnergy Society of Singapore (BESS). She is currently the Technology Development Manager and a Senior Lecturer at School of Life Sciences and Chemical Technology of Ngee Ann Polytechnic. Prior to joining Ngee Ann Polytechnic, she was working at Institute of Environmental Science and Engineering (IESE) as a research scientist. Dr. Geng obtained her Ph. D in Chemical and Environmental Engineering from the National University of Singapore (NUS) under government scholarship. She received her M. Eng and B. Eng degrees in Biochemical Engineering from Tianjin University, P. R. China. Dr. Geng has more than 20 years R&D experiences, working extensively environmental biotechnology, green energy technology and industrial biotechnology. She has more than twenty journal publications and her work has been presented in many international conferences. Her current research focus at Ngee Ann Polytechnic is on novel biocatalysts development for bioconversion of lignocelluloses to fuels and chemicals, industrial enzyme related technology development, and novel nutraceutical products development.

Abstract

Bioethanol is one of the biofuels. Unlike fossil fuels, ethanol is a renewable energy source produced through the fermentation of sugars. The first generation of bioethanol is derived from sugar- and starch-rich crops such as grains, corns, sugar cane and sugar beet etc. The second generation of bioethanol is extracted from materials that contain cellulosic biomass, such as hardwood, softwood, grasses and agricultural residues. It is therefore called as cellulosic ethanol. The material cost of cellulosic ethanol will be far less than that of the first-generation, and cellulosic biomass is the most abundant renewable source of sugars. Cellulosic ethanol is predicted to be more than doubled in yields without straining the food chain. It will also significantly improve energy efficiency and curb net CO2 emissions compared to the first-generation bioethanol. This presentation reviews the status of the cellulosic ethanol technology development and commercialization. The importance and roles of biocatalyst development will be addressed. R&D activities on cellulosic ethanol at Ngee Ann Polytechnic will also be discussed.